CreSP/I
\ˈkris-pē\

The Crestlength Storage Protocol/Interface

Copyright (c) 2016, Charles Thompson <chmithbiz@gmail.com>

Permission to use, copy, modify, and/or distribute this software for any purpose with or without fee is hereby granted, provided that the above copyright notice and this permission notice appear in all copies.
THE SOFTWARE IS PROVIDED "AS IS" AND THE AUTHOR DISCLAIMS ALL WARRANTIES WITH REGARD TO THIS SOFTWARE INCLUDING ALL IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS. IN NO EVENT SHALL THE AUTHOR BE LIABLE FOR ANY SPECIAL, DIRECT, INDIRECT, OR CONSEQUENTIAL DAMAGES OR ANY DAMAGES WHATSOEVER RESULTING FROM LOSS OF USE, DATA OR PROFITS, WHETHER IN AN ACTION OF CONTRACT, NEGLIGENCE OR OTHER TORTIOUS ACTION, ARISING OUT OF OR IN CONNECTION WITH THE USE OR PERFORMANCE OF THIS SOFTWARE

How CreSP/I Works
The Crestlength Storage Protocol and Interface encodes bytes by creating a square wave in which the length of the crest determines the value. The encoded data starts with a leader which gives the minimum crestlength (a crestlength that is equivalent to the value zero). The leader is ended with the maximum crestlength (255x the length of the minimum crestlength) and henceforth the data is read until the end of the recording.
Bytes encoded in CreSP are decoded by dividing the crestlength by the minimal crestlength and subtracting one.
Programs Provided
- acmp – optimizes data for CreSP storage.
- adec – processes data that has been optimized for CreSP storage; undoes the work of acmp.
- a2f – reads CreSP encoded data from raw unsigned 8-bit PCM files.
- f2a – encodes data into the CreSP and writes it to raw unsigned 8-bit PCM files.

acmp
pre-audio computation
optimizes data for the CreSP by representing the most common values with the lowest values
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34	#include "common.h" / int main( void ) / { / num *frqTbl = calloc(MVAL, sizeof(num)), tblSz = NUL, top = NUL, i; / byte *outTbl = calloc(MVAL, sizeof(byte)), buf = GET(); / for(;!EF; buf = GET()) / { / frqTbl[buf] ++; / if(frqTbl[buf] > frqTbl[top]) top = buf; / } / for(;tblSz < MVAL && frqTbl[top] != NUL;tblSz ++) / { / outTbl[tblSz] = top, frqTbl[top] = 0; / for(i = NUL; i < MVAL; i ++) if(frqTbl[i] > frqTbl[top]) top = i; / } / PUT(tblSz); / for(i = NUL; i < tblSz; i ++) / { / PUT(outTbl[i]); / frqTbl[outTbl[i]] = i; / } / fseek(stdin, 0, SEEK_SET); / for(buf = GET(); !EF; buf = GET()) PUT(frqTbl[buf]); / return 0; / }

adec
acmp decoder
decodes the data encoded by acmp.
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13	#include “common.h” / int main() / { / num tblSz = GET(), i = NUL; / byte *table = calloc(MVAL, sizeof(byte)), buf = GET(); / for(; i < tblSz && !EF; i ++, buf = GET()) table[i] = buf; / for(; !EF; buf = GET()) PUT(table[buf]); / return 0; / }

a2f
audio to file
decodes raw unsigned 8-bit pcm through CreSP and writes the product to stdout
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27 / 28 / 29 / 30 / 31 / 32 / 33 / 34 / 35 / 36 / 37 / 38 / 39 / 40 / 41 / 42 / 43 / 44	#include “common.h” / #define SKIP 200 /* The amount of bytes to skip in stdin */ / #define WCOR 1 /* The correction for getting an accurate minimal crestlength*/ / #define THRSH 50 /* The threshold to which it is considered part of a crest */ / #define RCONST 0.445 /* If a value is greater than this constant, it is / rounded up */ / num bLen = sizeof(byte); / num rounded(double di, double dv) / { / double d = di / dv; / num n = d; / double f = d - n; / return n + (f > RCONST); / } / num getWave() / { / num cLen = NUL; / while(GET() < THRSH && !EF); / while(GET() >= THRSH && !EF) cLen ++; / return rounded(cLen, bLen); / } / int main( void ) / { / byte buf; / fseek(stdin, SKIP, SEEK_SET); / getWave(); / bLen = getWave() + WCOR; / while(!EF && getWave() != LEND); / for(buf = getWave(); !EF; buf = getWave()) PUT(buf); / PUT(buf); / return 0; / }

f2a
file to audio
encodes stdin to CreSP and writes the raw unsigned 8-bit PCM to stdout
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12 / 13 / 14 / 15 / 16 / 17 / 18 / 19 / 20 / 21 / 22 / 23 / 24 / 25 / 26 / 27	#include "common.h" / #define TLEN 1 /* The length of the trough */ / #define HLEN 20000 /* The length of the header */ / #define AMP 200 /* The amperage */ / #define LCOR 1 /* Correction constant for genWave */ / void genWave(num len) / { / num tLen = TLEN; / while(tLen--) PUT(NUL); / while(len-- + LCOR) PUT(AMP); / } / int main( void ) / { / num hLen = HLEN, buf = GET(); / while(--hLen) genWave(NUL); / genWave(LEND); / for(; !EF; buf = GET()) genWave(buf); / return 0; / }

common.h
common inclusions and definitions
1 / 2 / 3 / 4 / 5 / 6 / 7 / 8 / 9 / 10 / 11 / 12	#include <stdio.h> / #include <stdlib.h> / #define PUT putchar / #define GET getchar / #define EF feof(stdin) / #define NUL 0 / #define LEND 255 / #define MVAL 256 / typedef unsigned int num; / typedef unsigned char byte;